## Slide 1
IPE 300
Industrial Practice
A presentation on
Presented By
1908021 - Abrar Hamim Masih
1908029 - Narayon Dey Noyon
1908047 - An-Nur Taiweb Rahman
1908050 - Muhammad Shadab Sakib
Presented To
Dr. Nikhil Ranjan Dhar
Professor, Department of IPE, BUET
Rashik Ahnaf
Lecturer, Department of IPE, BUET
Md. Tariqul Islam
DGM, HR, Knit Asia Ltd.
Industrial Attachment at Knit Asia Ltd

## Slide 2
Knit Asia Ltd
Founded in 1999, leading garment manufacturer in Bangladesh.
LEED-certified green factory, uses 50% solar power.
Supplies brands like Zara, Decathlon, and American Eagle; 200,000 garments/day.
Certified by WRAP, OEKO-TEX, and GOTS for sustainability.
Uses advanced 3D design tools like CLO and Optitex.

## Slide 3: Departmental Overview: Knit Asia Ltd.
Manages office logistics and supplies.
Coordinates communication and workflow between departments.
Implements and oversees company policies.
Organizes meetings and internal events.
Maintains office infrastructure and equipment.
Administration

## Slide 4: Departmental Overview: Knit Asia Ltd.
Maintains and updates employee records and databases.
Ensures adherence to labor laws and regulations.
Manages employee wages, benefits, and compensation.
Facilitates training and development programs.
Handles employee grievances and disciplinary actions.
Human Resource and Compliance

## Slide 5: Departmental Overview: Knit Asia Ltd.
Liaises with buyers and clients to showcase company capabilities and products.
Develops and implements pricing strategies.
Manages sample testing and product quality assessments.
Negotiates and finalizes order agreements.
Develops marketing materials and promotional strategies.
Marketing and Merchandising

## Slide 6: Production Process Flowchart: Knit Asia Ltd.
Spinning
Knitting
Dyeing
Cutting
Sewing
Finishing
Packaging

## Slide 7
Key insights from workers survey

## Slide 8: Positive & Negative Aspects
POSITIVES
NEGATIVES
Management address the safety concerns of the workers
Machines and different tools are well-maintained
Reluctant to use safety equipment
Familiar with the emergency evacuation procedures
Experience health issues, such as: back pain, neck pain due to prolonged sitting

## Slide 9
manpower utilization and removing bottleneck in a sewing line

## Slide 10
Time study
Average cycle time was calculated per operation
Table. Unbalanced time study sheet
Normal time = Avg. cycle time * rating
SMV = Normal time + Normal time * Allowance
Capacity = 60/SMV

## Slide 11
Finding bottleneck
Bottleneck occurs in 2nd, 14th,15th and 33rd process, where capacity is below 75pcs/hr
Fig. Unbalanced time study bar chart
Hourly production target 75 pcs/hr

## Slide 12
Proposed solution to remove bottleneck and utilize manpower
Work-share
U-shape layout
Replace worker in the bottleneck process
Change the machine layout
Assign an additional worker to the bottleneck area
Workstation
Product flow
Product flow
In
Out
Fig. U-shaped Sewing line

## Slide 13
After implementing aforementioned steps
Fig. Balanced time study bar chart
Bottleneck removed
Processes have capacity more than 75 pcs/hr
Extra capacity is used

## Slide 14
Ventilation sufficiency evaluation and eliminating dead spots on a sewing floor

## Slide 15
Importance of a comfortable work environment
Air Quality
Efficiency
Thermal Comfort

## Slide 16
Packaging Area
Exhaust Fans
Air Cooler
U-shaped Sewing Line
Ceiling Fans
Production (Sewing) Line Area (Usually well-ventilated and Controlled Temperature)
Packaging Platforms
Evaluating the ventilation system
Ceiling Fans | Exhaust Fans | Air Coolers
168 | 14 | 6
Quantity:
Ceiling Fans | Exhaust Fans | Air Coolers
2,000 | 3,000 | 18,000
Capacities in CFM:
Total Available CFM = 371,000 CFM
Floor Volume = 880,000 cu. ft
Total Number of People at a time = 1130
Figure: An Approximate Layout of the Sewing Floor
16

## Slide 17
Evaluating the ventilation system
A
= 25.3 (well over standard range of 6-12, ASHRAE 62.1)
Air Changes Per Hour
Required & Actual Ventilation
= 28,250 CFM (<<371,000 CFM)
Figure: An Approximate Layout of the Sewing Floor
17
Packaging Area
Exhaust Fans
Air Cooler
U-shaped Sewing Line
Ceiling Fans
Production (Sewing) Line Area (Usually well-ventilated and Controlled Temperature)
Packaging Platforms

## Slide 18
Presence of dead spots
Packaging Area (Many Dead Spots)
Exhaust Fans
Air Cooler
U-shaped Sewing Line
Ceiling Fans
Production (Sewing) Line Area (Usually well-ventilated and Controlled Temperature)
Packaging Platforms
Dead Spots
Several dead spots and hotter regions with lower airflow were observed on the sewing floor, particularly affecting workers in packaging and product handling areas.
Workers reported frequent discomfort and the need to pause and move to relieve heat-related stress.
Figure: An Approximate Layout of the Sewing Floor
18

## Slide 19
Packaging Area
Exhaust Fans
Air Cooler
U-shaped Sewing Line
Ceiling Fans
Production (Sewing) Line Area (Usually well-ventilated and Controlled Temperature)
Packaging Platforms
Potential changes to deal with dead spot issues
Additional Ventilation
Fan Repositioning
Air Cooler Repositioning
Exhaust Fan Optimization
Regular Maintenance
Figure: A Potential Updated Layout
19

## Slide 20
Layout Challenges in Washing & Dyeing Section

## Slide 21
14 Washing Machines
5 Deep Dyeing Machines
14 Drying machines
Current Layout

## Slide 22
Current Layout Challenges
Space Congestion
Material Handling
Deep Dyeing Machine Proximity
Heat Transfer
Water Pollution

## Slide 23: Proposed Layout
Average distance between Deep Dyeing and Washing: 36.42 to 41.94 meters
Average distance between Washing and Drying: 61.24 to 51.29 meters

## Slide 24: Proposed Layout Features
Lower Material Handling Cost
Improved Spacing
Line/Process Layout
Flow Efficiency

## Slide 25: Conclusion
Gained comprehensive understanding of RMG sector operations.
Developed communication, teamwork, and leadership skills.
Applied theoretical knowledge in real-world production scenarios.
Grateful to BUET and Knit Asia Ltd. for invaluable experience.

## Slide 26: Thank you

## Slide 27
Appendix

## Slide 28: Appendix A: Questionnaire for survey and the response

## Slide 29: Appendix A: Questionnaire for survey and the response

## Slide 30: Appendix B: Sample calculation of time study
For the 4th process which is side pocket zipper join-
Machine – Lock stich
Quantity processed = 7 pcs
Total time required = 196 sec
Average time =(Total time required)/(Quantity processed) =196/7 =28.0 sec
Worker rating = 100%
Normal time =Avg. time × worker rating =28.0×100% =28.0 sec
Allowance = 15%
Standard second value (SSV) =Normal time + Normal time ×Allowance (Niebel, 2009)
=28.0+28.0×15%
=32.20 sec
Standard minute value (SMV) =SSV/60 =32.20/60 =0.54 min
Capacity =3600/SSV =3600/0.54 =112 pcs/hr

## Slide 31: Appendix C: Matlab code
For current layout
For proposed layout